## Slide 1
ARM Inputs
ARM Outputs
freeRTOS_GPS_407
Applicatie: toont werking basale FreeRTOS-functionaliteit, zoals Queues, Tasknotification, Semaphores, Eventgroups, Interrupt-handling
NB. Admin.c/admin.h (hier niet getoond) bevat onder meer de initialisatie-routines van de FreeRTOS-tasks en -mechanismen.
Design: toont task-samenhang met communicatie- en synchronisatiemechanismen
Target: ARM Cortex M4 met STM32CubeIDE. (Auteur: MSC 2023)
ARM_keys_IRQ
EventGroupWaitBits(key) TaskNotifyGive(task, key)
LED_Task1 [priority A]
SemaphoreTake LEDs SemaphoreGive
LED_Task4 [priority C]
TaskNotifyTake SemaphoreTake LEDs SemaphoreGive TaskNotifyGive(T3)
ARM_keys_task
TaskNotifyTake(key) SemaphoreTake BUZZER, LEDs SemaphoreGive Color-LEDs
UART_keys_IRQ
QueueReceive(chars) wait for '\n' create string TaskNotifyGive(task,string)
EXTI0_IRQHandler [generated function]
ISR called key=KEYS_read() EventGroupSetBitsFromISR(key)
UART_menu
TaskNotifyTake(string) Handle commands, eg: toggle debug-setting output task data SetTaskPriority
HAL_UART_RxCpltCallback [generated function]
ISR called HAL_UART_Receive_IT(char) QueueSendFromISR(char)
ARM KBD
ARM UART
Via external PC
(terminal.exe)
ARM LEDs
ARM BUZZER
ARM
Color LEDs
ledjes.c
ARM_keys.c
LED_Task3 [priority B]
SemaphoreTake LEDs SemaphoreGive TaskNotifyGive(T4) TaskNotifyTake
STM32f4xx_it.c
LED_Task2 [priority A]
SemaphoreTake LEDs SemaphoreGive
UART_keys.c
main.c
note: same priority = round robin
ARM LCD
ARM UART